2.a. Truncated quantization

2.b. Rounded quantization

2.c. Whenever we use more bits to quantize a signal our error gets smaller; Also the difference between the floor and round quantization shows that all the errors are on truncated quantization are more on the positive side than the negative

2.d
Bits Used	SQNR Theory	SQNR Calculated
6	37.88	32.2076
7	43.90	38.1160
8	49.92	44.0617

%% Signal set up

clc;clear;close all;

%Constants

DSP_HW_2
amp = 1 ; %amplitude
fm = 1/8; %message frequency
time_start = 0;
time_end = 12;
fs = 1000;% Sampling frequency Hz
time = time_start:1/fs:time_end;
bits_to_use= 1:16; %
bits = bits_to_use(1:1:length(bits_to_use));
type = 2; %Quantization method floor = 1, round =2, ceiling = 3;

%Create a signal
sig_cont = sin(2*pi*time*fm);

%Allocate memory for error and SQNR arrays;
error = zeros(length(bits),length(sig_cont));
SQNR = zeros(1,length(bits));

%% Plotting multiple levels of quantization
for index = 1:length(bits);
    L= 2^(bits(index));

[sig_q,SQNR(index)] = quant(sig_cont,L,type);
error(index,:) = sig_cont-sig_q;
%if a value is within range of
min_err = min(error(1,:));
max_err = max(error(1,:));

%Original Signal
figure(1)
subplot (3,3,index +(index-1)*2)
plot (time,sig_cont);
title (['Original Signal']);
xlabel ('Time(s)')
ylim ([(-amp-amp/10) (amp+amp/10)]);

%Quantization Signal
subplot (3,3,index + 1+ (index-1)*2)
plot (time,sig_q,'--r')
title (['Quatizaiton with ', num2str(L), ' levels']);
xlabel ('Time(s)')
ylim ([(-amp-amp/10) (amp+amp/10)]);

%Error values
subplot (3,3,index+2+(index-1)*2)
plot (time,error(index,:),'black')
title (['Error rate using ', num2str(L), ' levels']);
xlabel ('Time(s)')
ylim ( [ (min_err - min_err/10) (max_err + max_err/10)])

end
%

%% SQNR Comparison
for index = 1:length(bits)
    L=2^(bits(index));
    [sig_q, SQNR(index)]= quant(sig_cont,L,type);
end;
SQNR_theory = 1.76+6.02*(bits)
SQNR
figure
plot (bits+1,SQNR_theory,'--',bits+1,SQNR,'*');
title ('SQNR Theoretical vs Caclulated ')
ylabel ('SQNR(db)');
xlabel ('Bits used');
legend ('Theory','Calculated');

%% SQNR
SQNR

%% END

 quant.m
function [sig_out,SQNRdb] = quant(sig_in,L,type)
%Quant Quantize a signal based on the function
% sig_in signal to quantize
% L levels of quantization
% type 1 for floor, 2 for round, 3 for ceiling

sig_max = max(sig_in);
sig_min = min(sig_in);
range = max(sig_in)-min(sig_in);
del = range/L ; %Step size

%Creating Bins for the values to go in and the
if type == 1 %Floor
    q_bins = sig_min : del :sig_max-del; %Creating Bins for the values to go in and the
    bin_location = min(L,floor((sig_in-sig_min)/del+1));%Determine the bin what the signal will go into

elseif type == 2
    q_bins = sig_min+del*1/2 : del :sig_max-del*1/2; %Creating Bins for the values to go in and the
    bin_location = min(L,round((sig_in-sig_min)/del+1));%Determine the bin what the signal will go into

elseif 3
    q_bins = sig_min+del : del :sig_max; %Creating Bins for the values to go in and the
    bin_location = min(L,ceil((sig_in-sig_min)/del+.1));%Determine the bin what the signal will go into

end

sig_out = q_bins(bin_location); %Assign the signal a value from the q_bins based on the bin_location
S0 = norm(sig_in);
N0 = norm(sig_in-sig_out);
SQNR = S0/N0;
SQNRdb =20*log10(SQNR);
end